## Slide 1: Time-of-Flight Coding
04/10/2019
Jonas Messner & Nicholas Gaudio

## Slide 2: Indirect Time-of-Flight Fundamentals

## Slide 3: ToF Imager Basics
  Source lights up a scene
    Light is a continuous wave
  Scene reflects light and light travels back to sensor
    Arriving light is a continuous wave
    Phase shift based on distance:
    Scene albedo:
    Ambient light:
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 4: ToF Imager Basics
  Sensor measures reflected light intensity
  Sensor exposure is varied according to demodulation function
  Measured brightness is the cross-correlation of and
    Paper:
    Def.:
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 5: ToF Imager Basics
  Measured brightness:
    Measured brightness is a function of albedo, ambient light, and correlation function
    Correlation function is a function of the modulation and demodulation functions
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 6: ToF Imager Basics
  Theoretically, any periodic modulation and demodulation function could be used to recover the depth of the scene.
  However: Noise disturbs the measurement
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 7: ToF Imager Basics
  Derivative of measured brightness over K measurements
    : Depth error std. deviation
    : Measurement (B) std. deviation
    : Correlation function
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 8: Coding Functions

## Slide 9: Coding Functions
  Equation shows that correlation function and thus modulation/demodulation functions inherently affect the depth measurement resolution, which is proportional to
  What is the ideal coding function for ToF imaging?
    Conventionally: sinusoid or square modulation/demodulation

## Slide 10: Coding Functions
Hypothesis: The longer the coding curve, the lower the depth error
: Depth precision measure
: Mean albedo factor
: Length of coding curve
: Std. dev. of intensity measurement
: Unambiguous depth range
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 11: Coding Functions
  Paper by M. Gupta et al. shows Hamiltonian coding
    Has better depth resolution than sinusoid and square
    Is not provably optimal
  Question: Can we use a Generative Adversarial Networks (GAN) in order to generate the ideal coding function depending on the scene?
Source: Mohit Gupta, Andreas Velten, Shree K. Nayar, and Eric Breitbach. 2018. What Are Optimal Coding Functions for Time-of-Flight Imaging?. ACM Trans. Graph. 37, 2, Article 13 (February 2018), 18 pages. DOI: https://doi.org/10.1145/3152155

## Slide 12: Project Idea

## Slide 13: Project Idea – Coding function design using DL
Generate
ToF data
Loss function
Input
RGB-D data
Groundtruth
Groundtruth
Coding functions
Albedo
Distance fall off
Noise
…
Coding functions:
1 modulation +
K demodulation
Raw → Depth

## Slide 14: Project Idea – Coding function design using DL
Backpropagate loss to adjust coding functions
Generate
ToF data
Loss function
Input
RGB-D data
Groundtruth
Coding functions:
1 modulation +
K demodulation
Raw → Depth
(CF / CNN)

## Slide 15: Project Idea – Coding function design using DL
  Start off simple… no neural network
  Pixelwise loss function that compares generated ToF image and groundtruth
  Number of demodulation functions (K) has to be greater or equal to 3
Generate
ToF data
Loss function
Input
RGB-D data
Groundtruth
Coding functions:
1 modulation +
K demodulation
Raw → Depth
(Closed Form)

## Slide 16: Project Idea – Coding function design using DL
  Replace closed form solution with CNN
    Can we reduce the number of demodulation functions to 2?
    How much does e.g. object recognition accuracy degrade?
Generate
ToF data
Loss function
Input
RGB-D data
Groundtruth
Coding functions:
1 modulation +
K demodulation
Raw → Depth
(CNN)

## Slide 17: Project Idea – Coding function design using DL
  Further considerations:
  Coding functions are setup as arbitrary signals (e.g. 100 data points each)
  Possible datasets (RGB-D data):
    NYU dataset (most common 3D dataset)
    SUN dataset
    Shapenet
    3D Face dataset?

## Slide 18: Project Idea – Coding function design using DL
  Goals:
    Find general optimal coding functions
    Find specific optimal coding functions
      E.g. for the scenario of 3D face recognition
      As all faces have similar shape there could be a special coding function that works particularly well for faces
    Compare the result to sinusoid, square and hamiltonian coding
    If simulator comes out: Simulate and compare

## Slide 19: Roadmap

## Slide 20: Roadmap
  Study the simulator
  Finalize dataset (Shapenet, Face-Dataset, NYU)
  Generate ToF image
    Perhaps adjust modeling to get better results
  Pixel-wise loss and backprop using the closed form solution for raw-to-depth
  Replace closed form solution with CNN

## Slide 21: Simulator Example

## Slide 22: Simulator Example – Sinusoidal Coding
Mean Squared Error: 1670.07

## Slide 23: Simulator Example – Hamiltonian Coding
Mean Squared Error: 112.77

## Slide 24: Simulator Example – Square Coding
Mean Squared Error: 630.01

## Slide 25: Simulator Example – How about different length pulses

## Slide 26: Simulator Example – How about different length pulses

## Slide 27: Simulator Example – Square Coding

## Slide 28: Simulator Example – Optimal Coding
?