## Slide 1
What are Optimal Coding Functions
for Time-of-Flight Imaging?
Support: ONR, DARPA
Mohit Gupta
Shree Nayar Andreas Velten Eric Breitbach
Notes: Alright, I am going to talk about time-of-flight cameras for 3D imaging.

## Slide 2
underwater exploration
3D Revolution
image courtesy: www.magicleap.com/, http://www.upi.com/
3D Imaging
robotic surgery
industrial automation
exploratory
robots
autonomous cars
augmented reality
Notes: 3D cameras are driving many new applications, self-driving cars, augmented reality, many different aspects of robotics and automation … there is a lot of excitement here...
As these applications mature, we are going to have scenarios which will require 3D imaging with increasingly high resolution..

## Slide 3
Extreme 3D Resolution
Stable Robot Navigation
Augmented Reality
Drone Control and Landing
Intricate Robotics
Notes: For example, think about an augmented reality setting…in order to get a real, immersive experience, we need to recover the 3D shape of surroundings with extreme detail…or imagine a drone flying through a forest --- it needs to resolve fine details like twigs and branches to navigate successfully…

## Slide 4
Rising Spatial Resolution, But Low Depth Resolution
3D Cameras: Spatial vs. Depth Resolution
Microsoft Kinect
Sony / SoftKinetic
Notes: I want to make a distinction between spatial and depth resolution…spatial resolution is just the number of pixels, and that continues to rise.
But, there are more fundamental limitations on the depth resolution--- which is the ability of a camera to differentiate two very similar depths.

## Slide 5
3D Imaging At Long Range
10 meters
3D ToF Camera
0.3 m
Object
Notes: Here is an example. Suppose a consumer grade 3D camera is looking at an object about 10 meters away.

## Slide 6
3D Shape: Current Consumer ToF Devices
Spatial Resolution 1 Megapixel
Depth Resolution ~1-2 Centimeters
* simulation result
Notes: This is the kind of 3D shape that it can expect to recover. Despite a high spatial resolution, the depth resolution is relatively low. So, we can may be tell that it’s a human face, but not much more.

## Slide 7
3D Cameras: Range vs. Resolution
1cm
1m
100m
10km
10cm
10m
1km
Measurement Range
Depth Resolution
1mm
10m
100m
1cm
10cm
camera
projector
Limited baseline
active triangulation

## Slide 8
3D Cameras: Range vs. Resolution
1cm
1m
100m
10km
10cm
10m
1km
Measurement Range
Depth Resolution
1mm
10m
100m
1cm
10cm
time-of-flight
source
sensor
modulated light
active triangulation
Notes: Talk about how ToF has an inherent advantage for large range imaging over structured light due to no baseline.
We cannot beat this trade-off…resolution will go down as range increases,
but, can we move this curve up…can we get 1-2 orders of magnitude higher resolution?

## Slide 9
Laser Scan Resolution at Long Distances
1cm
1m
100m
10km
10cm
10m
1km
Measurement Range
Depth Resolution
1mm
10m
100m
1cm
10cm
active triangulation
time-of-flight
Goal

## Slide 10
3D Shape: Our Goal
Spatial Resolution 1 Megapixel
Depth Resolution < 1 Millimeter at 10 meters Distance
* simulation result
Notes: Our goal is to get something like this, where there are sufficient details to perhaps start recognizing the person…
This will require cameras with an order-of-magnitude higher depth resolution as compared to current cameras – for example, at 10 meter distance, millimeters resolution instead of centimeters…

## Slide 11
Consumer 3D Imaging
“…The front 3D module could evolve toward
Time-of-Flight technology in the future…”
3D Imaging & Sensing – Market and Technology Report | www.yole.fr
Notes: If this were not challenging enough, we would like to do this with consumer-grade devices, so that these are broadly accessible, for example, in consumer imaging.
This sounds challenging, but fortunately, there is an imaging modality that is a good fit, at least a good starting point – and that is continuous wave time-of-flight imaging

## Slide 12
continuous temporally modulated light
Continuous Wave ToF Imaging
intensity
sinusoid
[Smith, 1980; Schwarte 1995; Lange, 2000]
scene
source
sensor
time
emitted light
Notes: Here is a typical continuous wave ToF camera. It consists of a light source and a sensor. The source emits light continuously – the intensity of the source is modulated over time at very high speeds. For example, the intensity could be modulated as a sinusoid over time.

## Slide 13
continuous temporally modulated light
received light
Continuous Wave ToF Imaging
phase-shifttravel distance (depth)
[Smith, 1980; Schwarte 1995; Lange, 2000]
source
scene
sensor
received light
demodulation function
demodulation function
measured brightness
intensity
emitted light
time
Direct Sampling Requires a Fast Sensor
Notes: The emitted light travels to the scene, and then, comes back to the sensor. Now, the brightness of the received light *also* varies as a sinusoid, but, the sinusoid is shifted in time. The amount of shift is proportional to the total travel distance, so, if we can measure the shift, we can compute the scene depth.
One way to do this is to directly sample the received sinusoid…but, this will require very high speed sampling, which is not very efficient or practical.
Instead, these cameras compute the correlation of this sinusoid with a demodulation function…which is typically also a sinusoid…this can be done much more efficiently…

## Slide 14
Measuring Phase-Shift: Correlation
Correlation:
measured
brightness
demodulation
function
received
light
received light
time
intensity
demodulation function
3 Unknowns: Phase, Offset, Amplitude
Notes: Eventually, the camera measures a single brightness value, which is the correlation of the received light and the demodulation function.
Now, a sinusoid has three unknowns, so, we need at least three measurements, which are taken by using three different demodulation functions.

## Slide 15
Measuring Phase-Shift: Correlation
Correlation 1:
demodulation functions
intensity
Correlation 2:
Correlation 3:
received light
time
Notes: From these measurements, we can recover the three unknowns, and then estimate the depths from the phase shift.
Alright, so this was a quick primer on how continuous wave time of flight cameras work…btw, this method is the basis of many consumer depth cameras, including the Microsoft Kinect and Sony Softkinectic.
So, at an abstract level, we can think of these cameras as a mapping from depth values to intensity values. This is an important point, so, I want to illustrate this…

## Slide 16
Correlation of two sinusoids is a sinusoid
Measuring Phase-Shift: Correlation
time
time
distance
Modulation Functions
Demodulation Functions
Correlation Functions
time
time
distance
d
Notes: Another way to think about this is in terms of the correlation function of the modulation and demodulation…
For a scene point which is at a distance d, the measured intensities are just the values of the correlation functions at distance d. This is an important point – so, I want to illustrate this a bit better…

## Slide 17
Mapping of Depth to Intensities
sensor
depth range
distance
Correlation Functions
d
3D Intensity Space
Notes: Consider a scene point at a distance d from the camera. The three intensity values I1, I2, I3 … captured by the camera are just the samples of the correlation functions…corresponding to that distance.
We can represent the three intensity values as a point in a 3-dimensional intensity space.

## Slide 18
Mapping of Depth to Intensities
Correlation Functions
distance
3D Intensity Space
depth range
sensor
d
Notes: If the scene is at a different distance, we get a different point in the intensity space…

## Slide 19
Mapping of Depth to Intensities
Correlation Functions
distance
3D Intensity Space
depth range
sensor
d
Notes: another distance, another different point.

## Slide 20
Space of All Possible Intensities
Correlation Functions
distance
Coding Curve
3D Intensity Space
depth range
sensor
Mapping from depths to measured intensities
Notes: So, essentially, if we look at all possible depth values, the map to a 1D set of intensity points that trace out a curve. We call this the coding curve.
Now, we can think of the coding curve as a geometric representation of a ToF camera design. The performance of any given ToF camera is determined by its correlation functions, which can be represented as a coding curve. So, we can explore the entire space of time of flight cameras in this geometrically intuitive space of coding curves.
From a functional stand-point, a coding curve defines a unique, one-to-one mapping from depths to intensities…

## Slide 21
Decoding: From Intensities to Depths
Correlation Functions
distance
decoding
decoding
3D Intensity Space
sensor
depth range
Coding Curve
Notes: Meaning every point on the curve corresponds to a depth, and vice versa…
So, if the camera measures an intensity point, we can use a decoding algorithm to compute the depth. A different intensity point, a different depth.
In the ideal case, if there is no noise, we can do this decoding perfectly…

## Slide 22
Effect of Noise on Decoding
large depth uncertainty low depth resolution
Correlation Functions
distance
decoding
3D Intensity Space
sensor
noise
Notes: …but, life is not ideal, there always is noise…meaning the actual measured intensity lies somewhere in a noise ball around the true intensity.
Because of this, there is always an uncertainty in the estimated depth, which can actually be quite large…this results in low depth resolution…
Just to emphasize…this is arguably the most important reason that limits the depth resolution of tof cameras…

## Slide 23
Increasing the Size of Intensity Space
Correlation Functions
distance
3D Intensity Space
sensor
noise
small depth uncertainty high depth resolution
Fixed Light Source Power
and Scene Brightness
Notes: One way to reduce the uncertainty is to increase the size of the intensity space…
If we could do this, then the same amount of noise will result in smaller depth uncertainty and higher depth resolution…
Unfortunately, increasing the size of the space requires increasing the scene brightness which we don’t have any control over, or increasing the light source power, which is also usually fixed due to a limited power budget.

## Slide 24
Key Idea: Longer Coding Curves
Correlation Functions
noise
3D Intensity Space
sensor
Longer Coding Curve
small depth uncertainty high depth resolution
distance
Notes: Now, let’s think about why we wanted to increase the size of the intensity space? It was actually to increase the length of the coding curve.
The main idea is that it is possible to have longer coding curves within the same space…for example this…now, this coding curve may have a different geometry and will require a different set of correlation functions…but, as long as these are physically realizable…we will get the benefits of longer curves, meaning lower uncertainty and higher resolution.

## Slide 25
mean signal
coding curve length
depth range
image noise
Unified Expression For Analyzing All CW-ToF Methods
Theoretical Expression for Depth Resolution
depth resolution
(higher the better)
Notes: In fact, we derived a theoretical expression that relates the coding curve length to the depth resolution…everything else being the same, the resolution is directly proportional to the coding curve length, up to a first order approximation...
Now, the coding curve length is a fairly intuitive geometric property, and is almost trivial to compute for any given continuous wave time of flight camera…
So, this single, common expression can be used to analyze the performance of many different ToF cameras…
Let’s look at a couple of examples..

## Slide 26
Example: Conventional Sinusoidal Coding
time
time
distance
Modulation Functions
Demodulation Functions
Correlation Functions
time
time
distance
Notes: One of the most popular tof camera designs uses sinusoid functions…for both modulation and demodulation…so, the correlation functions are also sinusoids……

## Slide 27
Example: Conventional Sinusoidal Coding
Coding Curve:
Circle of radius
( = number of
measurements)
Curve Length =
Intensity Space
Notes: In this case, the coding curve turns out to be a circle…with radius given by this expression…Here, K is the number of measurements…3 is the minimum, and a typical value is 4.
So, the coding curve length is just the circumference of the circle…
Okay, so, let’s compare this with another coding scheme…

## Slide 28
Example: Square Coding
time
time
distance
Modulation Functions
Demodulation Functions
Correlation Functions
time
time
distance
Notes: Where both modulation and demodulation functions are square waves…their correlation are these piecewise linear triangular functions….Any guesses what the coding curve looks like in this case?

## Slide 29
Example: Square Coding
Coding Curve:
Non-planar () polygon
Side length
Curve Length =
Intensity Space
Notes: It is actually a non-planar hexagon….in general, it is a polygon with 2K sides, the length of each side is 1/sqrt(K), so the total curve length is 2 times sqrt(K)….
So, now we can compare these two different schemes in terms of their coding curve lengths…

## Slide 30
Comparison
Curve Length =
Square Coding
Sinusoid Coding
Curve Length =
Resolution of square coding times
as compared to sinusoid coding
Notes: We take the ratio…and…
This suggests, that everything else being the same, square coding achieves twice as much resolution as sinusoid coding…we verify this using experiments which I’ll show later…
Now, this is only theoretical, because square coding requires higher bandwidth…but, this is just an example to demonstrate how different ToF camera designs can be analyzed using this geometric representation…
The next, perhaps more important question, is that can we use these geometric ideas to design new, high-performance cameras?

## Slide 31
Towards Optimal Time-of-Flight Coding
time
time
distance
Modulation Functions
Demodulation Functions
Correlation Functions
time
time
distance
?
?
?
?
?
?
?
?
?
Notes: One way to think about this is as an optimization problem in the space of modulation and demodulation functions…which is challenging because this is a high-dimensional space…Instead…

## Slide 32
Towards Optimal Time-of-Flight Coding
Optimize in the Space of Coding Curves
Intensity Space
Notes: What if we do this optimization directly in the geometric space of coding curves, which is more intuitive…
We know that long coding curves are better, so, let’s design some curves…

## Slide 33
Long Coding Curves
Self-Intersecting
Not Locality Preserving
Depths to Intensities Mapping Not Unique
Small Noise Can Result in Large Depth Errors
Notes: Here is one example…this is long, but it intersects itself. Meaning the mapping from depths to intensities is not unique. Okay – so, this is not good…
Here are two more candidates --- a helix, and a Hilbert space filling curve…both are long, don’t intersect with themselves…but, these are not distance preserving…meaning there are points on the curve that are close in the Euclidean sense, but far along the curve….so, even a small amount of noise can result in large errors….
Ideally we want a curve that is long, non self-intersecting, and has nice locality preserving properties.

## Slide 34
Long and Locality Preserving
Proposed: Hamiltonian Cycle on Hypercube
Coding Curve: Hamiltonian Cycle on Hypercube Graph
Nodes
Edges
Intensity Space
Curve Length =
Notes: One family of curves that satisfies all these properties is Hamiltonian cycles on hypercubes…We can think of the intensity cube as a graph…with vertices being the corners of the cube, and edges being the sides of the cube…
Then, we can make a Hamiltonian cycle that visits every corner of the cube exactly once….we remove the origin and the diagonal vertex for practical reasons…
This coding curve is quite long..in fact, its length increases exponentially as a function of K, the number of measurements…also, it has some nice, provable, distance preserving properties…meaning, if two points are close along the curve, then their Euclidean distance is also small, and vice versa…
Based on these ideas, we propose a new ToF design that uses the Hamiltonian cycle as the coding curve…Any guesses what the correlation functions look like?

## Slide 35
Hamiltonian Coding
Coding Curve
Intensity Space
Correlation Functions
distance
Notes: They have to be piecewise linear since the curve is piecewise linear…they look like trapezoidal functions…we can use these to implement tof cameras with this new design…
This is for three measurements. If we capture more measurements, for example 4 or 5, we look at Hamiltonian cycles on higher dimension cubes…4D or 5D

## Slide 36
Higher Order Hamiltonian Coding
distance
K=4 measurements
distance
K=5 measurements
Notes: And, the functions look like these…We can generalize these to any number of measurements…

## Slide 37
Relationship to Gray Codes
[000]
[001]
[011]
[010]
[110]
[111]
[101]
[100]
Gray Codes
Hamming Distance Between Consecutive Codes = 1
Noise Robust Communication
Notes: As an aside, Hamiltonian codes have an interesting relationship with binary Gray codes – these are a sequence of binary codes so that successive codes differ only in 1 bit…because of this property, these codes are highly robust to noise, and are widely used in digital communication…

## Slide 38
Relationship to Gray Codes
[000]
[001]
[011]
[010]
[110]
[111]
[101]
[100]
Gray Codes
Hamming Distance Between Consecutive Codes = 1
Robust Structured Light 3D Imaging
Gray code binary patterns
Captured Images
Scene
Notes: Also…in design of robust structured light 3D imaging systems…

## Slide 39
Relationship to Gray Codes
(0,0,0)
(0,0,1)
(0,1,1)
(0,1,0)
(1,0,0)
(1,0,1)
(1,1,1)
(1,1,0)
[000]
[001]
[011]
[010]
[110]
[111]
[101]
[100]
Gray Codes
Hamming Distance Between Consecutive Codes = 1
Notes: Now, one way to make Gray codes is to start with a hypercube…assign binary labels to every vertex, and then, visit every vertex along a Hamiltonian cycle…the order in which the vertices are visited, is a Gray code sequence…
Now, this must look familiar…we did something similar to design Hamiltonian functions…

## Slide 40
Hamiltonian Codes vs. Gray Codes
Gray Codes
Discrete
Hamiltonian Codes Continuous
Notes: the main difference…is that Gray codes are discrete, they correspond only to the vertices of the cube…whereas Hamiltonian codes are created using the entire continuous Hamiltonian cycle…
So, in a way, we can think of Hamiltonian codes as continuous generalization of the binary Gray codes, and because of that, inherit all the nice robustness properties of Gray codes…

## Slide 41
Comparison: Coding Curve Lengths
0
5
10
15
20
25
K (number of measurements)
Coding curve length
3
4
5
sinusoid
square
Hamiltonian
Notes: Earlier, we talked about coding curve lengths… Here, the x-axis is the number of measurements…, and the y-axis is the coding curve length. For sinusoid and square coding, the length increases as a function of sqrt(K).
For Hamiltonian, it increases exponentially…this suggests that we should be able to achieve much higher depth resolution with Hamiltonian codes…

## Slide 42
Simulation Results
Notes: Next, I want to show some results…starting with simulations..

## Slide 43
Fronto-Parallel Plane
Sphere
Depth Staircase
sensor
9.0 m
9.0 m
8.0 m
sensor
5.0 m
7.0 m
1.0 m
1.0 m
sensor
7.0 m
Scenes

## Slide 44
82
86
90
94
98
Depth (mm x 100)
Comparisons (K=5, Strong Noise)
sinusoid coding
(err = 206.7 mm)
square coding
(err = 136.1 mm)
Hamiltonian coding
(err = 23.4 mm)
Ground truth
pixel coordinate

## Slide 45
Comparisons (K=5, Strong Noise)
sinusoid coding
(err = 202.9 mm)
square coding
(err = 128.8 mm)
Hamiltonian coding
(err = 24.4 mm)
Ground truth
45
50
55
60
65
Depth (mm x 100)
pixel coordinate

## Slide 46
Comparisons (K=5, Strong Noise)
sinusoid coding
(err = 340.4 mm)
square coding
(err = 219.6 mm)
Hamiltonian coding
(err = 41.0 mm)
Ground truth
Depth (mm x 100)
65
70
75
80
85
90
pixel coordinate

## Slide 47
82
86
90
94
98
Depth (mm x 100)
Comparisons (K=5, Strong Noise)
sinusoid coding
(err = 206.7 mm)
square coding
(err = 136.1 mm)
Hamiltonian coding
(err = 23.4 mm)
Ground truth
pixel coordinate

## Slide 48
Comparisons (K=5, Strong Noise)
sinusoid coding
(err = 202.9 mm)
square coding
(err = 128.8 mm)
Hamiltonian coding
(err = 24.4 mm)
Ground truth
45
50
55
60
65
Depth (mm x 100)
pixel coordinate

## Slide 49
face
10.0 m
sensor
0.3 m
strong sunlight
Scene
Notes: Here is another example…a camera looking at a face about 10 meters away…

## Slide 50
sinusoid coding
(5 images)
Hamiltonian Coding
(5 images)
square coding
(5 images)
error = 14.51 mm
error = 8.07 mm
error = 1.46 mm
Comparison (Raw 3D Shape, No Processing)
Notes: These are the raw 3D shapes computed using different designs…with Hamiltonian coding, in this case, we get an order of magnitude higher precision…
We can apply some simple remeshing to these raw scans…to get this…

## Slide 51
sinusoid coding
(5 images)
Hamiltonian Coding
(5 images)
square coding
(5 images)
Comparison (After Remeshing)
Notes: With Hamiltonian coding, we recover sufficient details so that we can perhaps start recognizing the person…

## Slide 52
face
50 m
sensor
30 m
Scene: Long Distance 3D Imaging
strong sunlight
Notes: Here is another example…demonstrating long range 3D imaging…

## Slide 53
sinusoid coding
Hamiltonian Coding
error = 42.7 cm
error = 4.0 cm
Comparison
Notes: A comparison between sinusoid and Hamiltonian coding…if we zoom in…

## Slide 54
sinusoid coding
Hamiltonian Coding
Comparison (Close-Ups)
Notes: With Hamiltonian coding, we can make out intricate details like individual bricks…

## Slide 55
Largely limited to sinusoid / square coding
Time-of-Flight: Consumer Devices
Microsoft Kinect
PMD
Notes: Alright, so the next question is…how do we go from theory and simulations to a real implementation?
Current ToF cameras are mostly limited to sinusoid or square coding…So, to demonstrate our approach…

## Slide 56
Focusing Lens
Beamsplitter
Photodiode
Scene
Laser Diode with RF Control Input
Galvo Control Boards
Steering Mirrors
Amplifier
Galvo with Scan Lens
Implement Arbitrary Modulation / Demodulation Functions
(Bandwidth = 120 MHz.)
Hardware Prototype
Notes: …we developed a proof-of-concept prototype which can implement arbitrary modulation and demodulation functions…There is a laser diode that emits light which goes to the scene, and then comes back to a sensor…which is currently a single pixel. We capture an entire scene by scanning the pixel…

## Slide 57
Galvo Waveform Generator
Modulation/ Demodulation Function Generator
Mixer
Photodiode
Laser Diode
Oscilloscope
Laser Diode Current Controller
Hardware Prototype
Miniaturize on Chip?
Notes: There are many other components….but, we hope that eventually, this will be miniaturized on chip…Next, I want to show some real experimental results..

## Slide 58
sensor
planar patches
80 cms
d = 2.5 cms
d
d
z
x
y
Scene
Notes: Here is a staircase kind of scene with three planar patches at different depths…

## Slide 59
sinusoid coding (5 images)
Hamiltonian coding (5 images)
mean error = 11.4 mm
mean error = 2.4 mm
Comparisons
Notes: This is a comparison of the recovered depths…the staircase structure seems to be lost with sinusoid, but recovered reasonably well with Hamiltonian….note that the improvement in real experiment is lower than simulations because our current hardware prototype is not optimized to implement Hamiltonian coding…

## Slide 60
sinusoid coding
Hamiltonian coding
Object
Comparisons with Low Power Source
Notes: Here is another example…demonstrating that Hamiltonian coding can recover geometry reliably even with a very low power light source…

## Slide 61
Correlation Functions
(three out of K)
Multi-Frequency Sinusoid Coding
Coding Curve
(“artist’s impression”)
Not Locality Preserving: Large Errors due to Small Noise

## Slide 62
Comparisons
Low Noise
Medium Noise
High Noise
Hamiltonian
[RMSE = 3.0 mm]
[RMSE = 12.4 mm]
[RMSE = 16.9 mm]
multi-freq sine
[RMSE = 3.6 mm]
[RMSE = 231.2 mm]
[RMSE = 509.9 mm]
Performance degrades rapidly

## Slide 63
Discussion: Current Implementation
time
time
distance
Modulation
Demodulation
Correlation
time
time
distance
Impulse function
Impulse function
Impulse function
Inefficient
Impulse function
Impulse function
Impulse function

## Slide 64
Discussion: Practical Implementation
time
time
time
time
distance
distance
Modulation
Demodulation
Correlation
Practical
Square function
Sqaure function
Square function

## Slide 65
Summary
High Precision Long Range 3D Scanning
Coding Space Theory of ToF Imaging
Prototype: ToF 3D Imaging System
Range vs. Resolution: 3D Imaging
Notes: In summary, we talked about designing 3D cameras that can achieve high resolution even at long distances. We talked about a new coding space theory and geometric tools for analysis and design of ToF cameras.
Based on this, we developed a new family of camera designs that can do high precision 3D scanning at long ranges; we showed a few example results using simulations and a hardware prototype…

## Slide 66
Coding Curve Design Contest: Optimal ToF?
http://wisionlab.cs.wisc.edu/project/tofcoding/
Higher Performance Curves?
Notes: Before I finish, I want to emphasize that the new camera designs are by no means optimal…
Using this geometric analysis, it may be possible to design curves that can do better…These could be small perturbations of Hamiltonian curves, or, maybe something completely different…If you have some ideas, I would love to talk with you.
Thank you very much for listening, and I will be happy to take any questions…

## Slide 67
Depth Staircase
7.0 m
1.0 m
1.0 m
sensor
7.0 m
Scene
Notes: This is a staircase…

## Slide 68
Comparisons: Strong Noise (K=5)
sinusoid coding
[error = 340.4 mm]
square coding
[error = 219.6 mm]
Hamiltonian coding
[error = 41.0 mm]
Ground truth
Depth (mm x 100)
65
70
75
80
85
90
pixel coordinate
Notes: This is the ground-truth depths along a vertical scan-line…
These are the shapes recovered using conventional sinusoid and square coding..there is a lot of noise here due to strong ambient light…as we can see, the underlying staircase geometry is almost completely lost…
With the same total power and capture time; Hamiltonian coding recovers the staircase…
An improvement like this could make a qualitative difference, perhaps enabling a robot to successfully climb the staircase…